## Slide 1
Basic Electronics
Basics of transistors

## Slide 2
BJT Relationships - Equations
B
C
E
IE
IC
IB
-
+
VBE
VBC
+
-
+
-
VCE
B
C
E
IE
IC
IB
-
+
VEB
VCB
+
-
+
-
VEC
npn
IE = IB + IC
VCE = -VBC + VBE
pnp
IE = IB + IC
VEC = VEB - VCB
Note: The equations seen above are for the transistor, not the circuit.

## Slide 3: Bipolar Junction Transistors: Basics
Bias Mode | E-B Junction | C-B Junction
Saturation | Forward | Forward
Active | Forward | Reverse
Inverted | Reverse | Forward
Cutoff | Reverse | Reverse

## Slide 4: Operation of npn transistor
Large current

## Slide 5
Modes of operation of a BJT transistor
Mode BE junction BC junction
cutoff reverse biased reverse biased
linear(active) forward biased reverse biased
saturation forward biased forward b

## Slide 6: Operation of npn tra nsistor (active mode)
Large current

## Slide 7
Summary of npn transistor behavior
npn
collector
emitter
base
IB
IE
IC
small
current
large current
+
VBE
-

## Slide 8
Summary of pnp transistor behavior
pnp
collector
emitter
base
IB
IE
IC
small
current
large current
+
VBE
-

## Slide 9
Summary of equations for a BJT
IE  IC
IC = bIB
b is the current gain of the transistor  100
VBE = 0.7V(npn)
VBE = -0.7V(pnp)

## Slide 10: 4.5 Graphical representation of transistor characteristics
IB
IC
IE
Output
circuit
Input
circuit

## Slide 11: Input characteristics
Acts as a diode
VBE 0.7V
IB
IB
VBE
0.7V

## Slide 12
Output characteristics
IC
IC
VCE
IB = 10mA
IB = 20mA
IB = 30mA
IB = 40mA
Cutoff
region
At a fixed IB, IC is not dependent on VCE
Slope of output characteristics in linear region is near 0 (scale exaggerated)
Early voltage

## Slide 13
Biasing a transistor
Transistor Biasing is the process of setting a transistors DC operating voltage or current conditions to the correct level so that any AC input signal can be amplified correctly by the transistor. A transistors steady state of operation depends a great deal on its base current, collector voltage, and collector current and therefore, if a transistor is to operate as a linear amplifier, it must be properly biased to have a suitable operating point .We must operate the transistor in the linear region.
A transistor’s operating point (Q-point) is defined by
IC, VCE, and IB.

## Slide 14
Modes of Operation
Most important mode of operation
Central to amplifier operation
The region where current curves are practically flat
Active:
Saturation:
Barrier potential of the junctions cancel each other out causing a virtual short
Cutoff:
Current reduced to zero
Ideal transistor behaves like an open switch
* Note: There is also a mode of operation called inverse active, but it is rarely used.

## Slide 15: BJT configurations
GAIN
CONFIG

## Slide 16
Three Types of BJT Biasing
Biasing the transistor refers to applying voltage to get the transistor to achieve certain operating conditions.
Common-Base Biasing (CB) : input = VEB & IE
output = VCB & IC
Common-Emitter Biasing (CE): input = VBE & IB
output = VCE & IC
Common-Collector Biasing (CC): input = VBC & IB
output = VEC & IE

## Slide 17
Common-Base
Although the Common-Base configuration is not the most common biasing type, it is often helpful in the understanding of how the BJT works.
Emitter-Current Curves
Saturation Region
IE
IC
VCB
Active Region
Cutoff
IE = 0

## Slide 18
Common-Emitter
Collector-Current Curves
VCE
IC
Active Region
IB
Saturation Region
Cutoff Region
IB = 0

## Slide 19
Common-Collector
Emitter-Current Curves
VCE
IE
Active Region
IB
Saturation Region
Cutoff Region
IB = 0
The Common-Collector biasing circuit is basically equivalent to the common-emitter biased circuit except instead of looking at IC as a function of VCE and IB we are looking at IE.
Also, since  ~ 1, and  = IC/IE that means IC~IE

## Slide 20
DC  and DC 
 = Common-emitter current gain
 = Common-base current gain
 = IC  = IC
IB IE
The relationships between the two parameters are:
 =   = 
 + 1 1 - 
Note:  and  are sometimes referred to as dc and dc because the relationships being dealt with in the BJT are DC.